An Investigation into the Application of Edge Detection to Detect Cells
# Aim
The aim of this experiment is to contrast and compare the suitability of various edge detection algorithms and their application in serological testing for anti-nuclear antibodies. The edge detection methods that will be investigated in this experiment are as follows: Simple gradient, Roberts, Sobel, first order Gaussian. Laplacian and Laplacian of Gaussian. The results of each will then be compared using Receiver Operator Check analysis so that a conclusion can be drawn.
# Method
In order to perform edge detection, first a single image matrix must be produced from the colour images provided as the colour images comprise of 3 separate red, green, blue (RGB) matrices. This is done by taking only the green channel of the image as the cells being detected fluoresce green. After an image matrix has been created smoothing can be applied if required and an edge detection algorithm can be applied.

## First Order Derivative Edge Detection
First order derivative edge detection approximates the gradient of an image, after the gradient of an image has been calculate the areas of change within the image are then apparent. These areas of change are normally associated with edges therefore by thresholding the gradient values with a suitable threshold the edges of the image can be found.

### Simple Gradient:
Simple gradient first calculates the vertical gradient and horizontal gradient of the image, to calculate the vertical gradient the image is convolved with and to calculate the horizontal gradient convolve the image with . After getting both the horizontal and vertical gradient an approximation for the image gradient can be made by finding the magnitude of the two gradient matrices using .

### First order derivative of Gaussian:
The first order derivative of Gaussian is similar to the simple gradient technique except that before applying the simple gradient technique the image is convolved with a Gaussian like simple gradient but convolve the filters with a Gaussian filter before application. This has the effect of removing noise from the image which should remove the number of false positives in the edge detection.

### Sobel:
Sobel utilises a three by three matrices to approximate horizontal and vertical gradients, this has the advantage of there being a centre to the matrices which retains the positioning of the gradients instead of shifting the positions which happens when using a 2x2 matrix. The image is then convolved with the matrix to find the horizontal gradient image and with to find the vertical gradient image. The image gradient can then be approximated using the same technique described in simple gradient.
### Roberts:
The Roberts edge detection method approximates the gradient of an image by first finding the differences between diagonally adjacent pixels. This is done using two 2x2 matrix and convolving them with the original image to form and . These are both gradient components of the image which are finally used to calculate a gradient magnitude with .

## Second Order Derivative Edge Detection
Second order derivative edge detection approximates the rate of change of gradient in a given image, after this has been found the point at which there is a crossing from negative to positive change can be detected, this represents an edge in the image. As each time a derivative is taken noise in the image is amplified second order derivative edge detection is considered bad for noisy images unless smoothing is applied.

### Laplacian
Laplacian edge detection utilises only a single matrix in order to approximate changes in gradient of an image. The matrix is convolved with the image matrix to create a matrix representing the change in gradient. The edges are then detected by finding the points where there is a change from negative to positive in the matrix.

### Laplacian of Gaussian
The Laplacian of Gaussian method is similar to the Laplacian method except a Gaussian matrix is first convolved with the edge detection matrix described above. After this has happened the resulting matrix is convolved with the image matrix and edges are found in the same manner as Laplacian. This has the effect of smoothing the image at the same time as applying Laplacian edge detection therefore removing noise from the image and false positives from the edge detection.
# Results

# Conclusion